## Slide 1: EE209 - Fundamentals of Electrical & Electronics Engineering
M. Mert ANKARALI, PhD

## Slide 2: Typical electrical circuit
Interconnection of electrical elements

## Slide 3: A more generalized view
Take the real world problem

## Slide 4: A more generalized view
Simplify and represent it with a graphical model
The art of engineering

## Slide 5: A more generalized view
Represent the graphical model using a parametric mathematical model and solve (i.e. analyze)

## Slide 6: Not limited to electrical circuits
Thermal modeling of a thruster

## Slide 7: Not limited to electrical circuits
Mechanical modeling of a magnetic levitation train

## Slide 8: Electrical Charge
“Electric charge is the physical property of matter that causes it to experience a force when placed in an electromagnetic field” [https://en.wikipedia.org/wiki/Electric_charge]
The unit of charge is Columbs (C), which is equal to charge of 6.24×1018 electrons

## Slide 9: Electrical Current
Current is the rate of charge
  Charge is carried by moving electrons
Unit of electrical current is Ampere (A)
  1 A = 1 C/sec

## Slide 10: Voltage Difference
Voltage is related to the strength of the electric field
  Analogous to pressure in a hydraulic circuit
Voltage is always measured between two points, that is why it is also called potential difference.

## Slide 11: Analogy between electrical and hydraulic circuits
Voltage Difference = Pressure Difference
Electrical Current = Water Current
Resistance = Tap/Pipe Resistance

## Slide 12: Power
P: Rate of change of energy (dissipating or absorbing)
Power of unit is Watt (W)

## Slide 13: Energy
w: Unit of energy is Joules
  Integral of power over time
It is also common to to express electrical energy in kilo-watt hours (kWh).

## Slide 14: Resistance & Resistivity
Electrical resistance is the reaction/resistance of a conductor to an electrical current/flow
  Voltage drop
Hydraulic resistance is the reaction/resistance of an element to the water current/flow
  Pressure drop
Unit of electrical resistance is Ohm (Ω)
Resistance of an ideal uniform cable
L: length, A: Area, ρρ: Resistivity ( unit: Ω.m)
Ideal resistance in general ?

## Slide 15: Ohm’s Law
There is a static/memoryless linear relationship between the flow current and voltage drop across a resistor

## Slide 16: What is the best conductor?
Aluminium: 2.8210−8 Ω.m
Copper: 1.6810−8 Ω.m
Silver: 1.5910−8 Ω.m

## Slide 17: What is the best conductor?
Aluminium: 2.8210−8 Ω.m
Copper: 1.6810−8 Ω.m
Silver: 1.5910−8 Ω.m
Gold: 2.4410−8 Ω.m
Why gold?

## Slide 18: What is the best conductor?
Aluminium: 2.8210−8 Ω.m
Copper: 1.6810−8 Ω.m
Silver: 1.5910−8 Ω.m
Gold: 2.4410−8 Ω.m
Why gold?
Corrosion

## Slide 19: Terms in circuit diagrams
Node: Point of connection between elements.
Branch: Connection between two nodes.
Loop: Closed loops in circuit diagram.
Number of Branches = # of Loops + # of Nodes - 1

## Slide 20: Kirchhoff's Current Law
Algebraic sum of currents entering a closed a node (or a loop) is zero

## Slide 21: Kirchhoff's Voltage Law
Algebraic sum of all voltages around a closed path (or loop) is zero.

## Slide 22: Series resistors

## Slide 23: Parallel resistors

## Slide 24: Parallel resistors
Two resistors

## Slide 25: Connection of Voltage Sources
Series voltage

## Slide 26: Connection of Voltage Sources
Parallel voltage

## Slide 27: Connection of current sources
Parallel current source

## Slide 28: Connection of current sources
Series current source

## Slide 29: Passive sign convention
(Passive) resistors cannot produce power, only consumes it !
!Current enters the positive voltage terminal

## Slide 30: Power
(Passive) resistors cannot produce power, only consumes it !
Absorbed Power for a Resistor > 0

## Slide 31: Short/Open circuit
Short circuit: Resistance & voltage drop
Open circuit: Resistance & current

## Slide 32: Questions ?